Alternator Testing Procedure   1996 Subaru SVX

Using a 12V power socket with two battery clamps at the other end, I connected the socket to the POS and NEG terminals of my battery and plugged in my Nordskog digital voltmeter. This had the additional, upgraded 4 gauge power and ground wires.

I believe that by connecting the meter as close to the alternator as possible, I would get the most accurate readings. Since there is only one wire directly from the alternator output terminal to the battery, this would be the optimum location for testing.

Next, start the car with all accessories off and check the voltage level. It should be between 13.5 and 14.5 volts. (it depends on your make and model of car) My particular installation gives me a 14.3V reading (cold condition)

The main thing I am looking for is a drop in voltage. Once I hit around 12.5V, the alternator is not going to produce any additional amperage.

The next thing I do is turn on one accessory at a time. I also have a chart of the fuse rating for each accessory that I use. I keep turning on accessories and adding up the fuse ratings until the voltage falls to 12.5V

If my electric cooling fans are on, I add an additional 25A for these, and an additional 10 amps for the battery. Here are the fuse ratings for my car:

      10A	Battery -10A
      25A	Cooling fans (at startup)
      30A	Headlights
      10A 	High Beams

10A	Tail lights

20A	Brake lights

10A	Air Conditioning

15A	A/C Fans
20A	Rear Defroster

20A	Heated Mirrors

15A	Stereo system

The combined total fuse ratings of the above circuits adds up to 185A

I have used most of these simultaneously in various combinations with my stock 95A alternator and never had a problem. Likewise, I have NEVER blown a fuse in any of these circuits, so I am certain that the fuses are rated at much higher than the actual current draw for each circuit.

So it seems that my electrical system used much less than this, as the stock alternator charging system was rated at 95A at full output and about 40A at idle.

Adding other small circuits (flashers, wipers, etc.) and the total electrical load on my system could be between 40-60A.

The fact that I have had an 80A inline fuse in the car for more than two years without blowing them, both with the stock alternator and the high-output one, seems to support these figures.

Having my 160A alternator, producing over 80A at idle is what this is all about in addressing my original concerns of power in a low-speed situation.

I did all of these measurements at 800rpm idle and at 2000 rpm. This way I tested idle output and maximum.

Assuming a “hot state” decrease in output of 80% of maximum, I still have 70A available at idle and 136A at 2000rpm with the high-output alternator