Installing the OEM CD stacker.

Going on to www.jauce.com 12 months ago I picked up the CD stacker for about NZ$30, with some other stuff that I had bought.

I already had the CD stacker controller together with a JDM radio from an earlier buy at Jauce.

Having the spare parts manuals I located the correct  OEM “screws”  - they turned out to be zinc plated self-tappers. I added the 6mm dia. Stainless steel spring washers.

I was still looking for the wiring loom to connect them up – the wrecked SVXs I have been to over the past 6 months already had wiring looms removed and the parts manuals only showed the radio/cd/cd controller and stacker.

The mounting frame was a bit rusty – I got it stripped/dipped and then painted in black zinc to stop any new corrosion.

Even though I have owned the car for over 22 years, I have never had the need to remove the boot liner – the car was NZ new in 1995 and the original owner must have specified a single CD player and radio in the centre console.

The car came with the CD stacker hinged door and even when I fitted USA rear side markers (they have lights inside as opposed to NZ which only got them as reflectors – no holes in the rear housing) I could not see any wiring connector for the Stacker unit.

About 6 months ago I noticed moisture in the rear lights, so after removing them I noticed a connector and by removing the boot rubber seal and then carefully pushing the rear liner towards the centre of the car, you unclip the liner (which I then pushed forward to better see the wiring loom and the connector).

The CD stacker mounts at 3-points (in my car there were 3 circular black stick-on dots) – I used a small screwdriver to break through the stickers, and then measured the opening as 10mm square. I went down to my local hardware store and picked up 3 white square grommets of 3/8” - that had a hole in the middle and they have approx. 12mm circular top-hat, they expand slightly as the screw is inserted.

The twisted red/black wires are for the USA rear markers – I simply joined them into the existing rear red (on at night) lights.

Photo on the right clearly shows mated connector and also the 3rd mounting screw just behind it.

Hopefully if I get time over Xmas I will install the CD controller unit, in the mean time I still have the OEM single CD player.