Making up a SVX Transmission Pressure Gauge

The following information has been provided by Trevor Sheffield

I purchased a cheap but excellent Japanese gauge, together with brass fittings and very thin HP plastic tubing. The SVX test port has a 10 x 1mm straight thread and, from memory, it is located in a recessed area between the transmission casing and the engine crankcase, on the left side.

It is fitted with a removable threaded plug. If you are unable to find a suitable attachment fitting, modify the plug as I did by drilling and brazing in a short piece of tubing.

A company which markets hydraulic fittings is your best bet. I have racked my brain, talked to Google and am sure that I have located the gauge I used. Go to the links below and check the $15.00 dollar item. I used a back entry type. The same thing must be available in most parts of the world from a similar supplier

http://www.cps.co.nz/shop/gauges/40-mm-gauges/15-inch-brass-internal-dry-gauge/P140/C33

http://www.cps.co.nz/shop/gauges/40-mm-gauges/C33