The "Check Engine Light" indicates transmission codes. Long blinks = 10, short blinks = 1. In other words, two long and two short blinks is a code 22. One long and one short is code 11.

### The following self diagnosis will show any fault codes for the engine:

Remove the kick panel just beside the left foot rest on the driver's side. Locate blue wires.

Locate black connector (the smaller of the 2 black ones). Hold it notch up.

With ignition off, insert one of the wires into top row, 2nd pin from the left.

Turn key to “ON” position, but do not start the car.

Count the blinks from Check Engine light on dashboard.

### To clear codes (after problem has been resolved):

With engine off, stick the blue wires to 1st and 2nd pin in the top row counting from left on the black connector, with notch facing up.

Start car. Shut off car. Remove pins.

Read codes to make sure they are clear. No codes = steady blinks at 1/4 second intervals.

List of ECU Trouble Codes

Code	 Item	Diagnosis

11	Crank angle sensor 1     	No signal from crank angle sensor 1 for more than

3 seconds after start switch on.

12	Starter switch	Abnormal signal from ignition switch.

13	Cam angle sensor	No signal from cam angle sensor, but signal

from crank angle sensor 1.

14	Injector #1	Fuel injector inoperative.

(Abnormal signal from monitor circuit.)

15	Injector #2	Fuel injector inoperative

16	Injector #3	Fuel injector inoperative

17	Injector #4	Fuel injector inoperative

18	Injector #5	Fuel injector inoperative

19	Injector #6	Fuel injector inoperative

21	Water Temperature

Sensor	Abnormal signal from water temperature sensor.

22	Knock sensor 1 (RH)		 Abnormal voltage in knock sensor monitor circuit.

23	Air flow sensor		Abnormal voltage from air flow sensor.

24	By-pass air control		By-pass air control solenoid valve inoperative.

solenoid valve			(Abnormal signal in monitor circuit.)

28	Knock sensor 2 (LH)		Abnormal voltage in knock sensor monitor circuit.

29	Crank angle sensor 2		No signal from crank angle sensor 2, but two

signals from crank angle sensor 1.

31	Throttle sensor		Abnormal voltage from throttle sensor.

32	O2 sensor 1 (RH)		O2 sensor 1 inoperative.

33	Vehicle speed sensor 2	No signal from vehicle speed sensor 2.

34	EGR solenoid valve		EGR solenoid valve inoperative.

35	Purge control solenoid

valve				Purge control solenoid valve inoperative.

37	O2 sensor 2 (LH)		O2 sensor 2 inoperative.

38	Engine torque control		Wiring harness between ECU and TCU is in short circuit.

41	A/F learning control		Faulty learning control function.

45	Atmospheric pressure

Sensor				Faulty atmospheric pressure sensor inside ECU.

51	Neutral switch			Abnormal signal from inhibitor switch.

52	Parking switch			Abnormal signal from parking switch.

55 	EGR Gas temperature

Sensor (CAL.)			Abnormal signal from EGR gas temperature

56	EGR system (CAL.)		EGR calve open/close stick, EGR hose disconnected or

exhaust pressure valve damaged.