Rear Gear Swapping

- Remove the SVX rear differential.

- Remove the rear differential cover plate. 8 bolts

- Remove both side plates from the rear differential.

- Remove the LSD from the rear carriage.

- Remove the 8 bolts holding the ring onto the LSD.

- Install desired ring gear, i.e. 4.11 or 4.44 onto LSD

- Tighten and torque the 8 bolt on the LSD

- Place the rear carriage onto its end so that the tail is up.

- Remove the large nut that holds the pinion into the carriage.

  - Use an electric or pneumatic impact gun for this if you can.

  - Hold the driveshaft flange with a rubber strap.

- Place a 2x6 piece of wood under the rear of the carriage.

- Use a drift and hammer to drive the pinion out of the rear carriage.

- Install the desired pinion into the SVX carriage and tighten and torque.

- Install the reassembled LSD with the matching ring into the SVX carriage.

- Install side plates and torque bolts.

- Install rear cover plate and torque bolts.

- Fill differential with new LSD gear lube.

- Install the differential back into the SVX

This is what I did with mine. I did not have to do any grinding onto the rear carriage. The whole process took about one hour with slight problems.