How to' for 4WS codes

For those very few who have RHD and 4WS, here are the codes for 
deciphering the 4WS check light.

1) Remove the kick panel just beside accelerator pedal. 
2) Locate blue wires. 
3) Locate black connector. Hold it so that the notch is up. 
4) With ignition off, insert one (either one) of the blue wires into 
top row, 4th pin from left. (The black connector has 4 pins in the top 
row and six in the bottom row) 
5) Turn key to on position, but do not start the car. 
6) Watch flashing 4WS light on dashboard. Count blinks. Long blinks = 
10, Short blinks = 1. 
7) Keep watching flashing light until you have remembered the 
code/codes

CODE PROBABLE CAUSE

11 Speed sensor - cut/short 
13 Steering Wheel Angle Sensor - off centre 
14 4WS ECU - no power 
21 Steering Wheel Angle Sensor - cut/short or sensor failed 
22 Steering Wheel Angle Speed Sensor - cut/short 
31 Rear Wheel Steering Sensor and Motor - failed 
32 Rear Wheel Steering Sensor - cut/short? or sensor failed 
33 Rear Wheel Steering Speed Sensor - cut/short or sensor failed 
34,37 Rear Steering Motor - no power 
35 Rear Wheel Steering locked due to short in Steering Motor 
36 Rear Steering - Left/Right Lock has been exceeded. 
41, 43, 44 4WS ECU failed 
42 Rear Wheel Steering Motor - no power due to blown fuse 
45 Rear Wheel Steering Motor short, ECU failed

To clear codes (after problem has been resolved):

1) Ignition 'OFF' 
2) Remove Fuse SBF7 (4WS) from Fuse Box in Engine Bay. Wait 5 minutes. 
3) Reinsert fuse. 
4) Recheck as above to ensure all codes have been cleared. No codes = 
steady blinks at 1/4 second intervals.