Torque Specs

| 15 minute/$15 mod | 39-48 ft/lb |
| --- | --- |
| 2 bolts on timing belt adjuster | 17-20 ft/lb |
| 2 rear diff mount nuts | 45-56 ft/lb |
| 3 nuts for trans mount | 20-35 ft/lb |
| All cam belt sprockets/pulleys | 14-22 ft/lb |
| Axle nuts | 123-152 ft/lb |
| Ball joint to ctrl. arm | 79-101 ft/lb |
| Ball joint to knuckle | 33-43 ft/lb |
| Bell housing bolts and nuts | 34-40 ft/lb |
| Crankshaft pulley | 108-123 ft/lb |
| Drive shaft flange | 17-24 ft/lb |
| Driveshaft carrier bearing bolts | 35-42 ft/lb |
| Flexplate to Crankshaft | 51-55 ft/lb |
| Intake manifold to block | 17-20 ft/lb |
| Pinch bolt on lower control arm | 33-43 ft/lb |
| Pitch stopper | 27-31 ft/lb |
| Rear diff (2) long and (4) short bolts | 94-116 ft/lb |
| Spark plugs | 14-22 ft/lb |
| Torque converter to flex plate | 17-20 ft/lb |
| Trans crossmember to body | 40-61 ft/lb |
| Trans mount Castle nut | 17-27 ft/lb |
| Trans mount to trans | 13-23 ft/lb |
| Trans crossmember to Trans mount | 20-35 ft/lb |
| Wheel nuts | 69-83 ft/lb |